## Slide 1
Jason-1 orbit comparison :
POE-E versus POE-D
L. Zawadzki, M. Ablain (CLS)

## Slide 2
Objectives
Evaluate POE-E orbit for Jason-1 (by comparison to POE-D standard)
Observe and analyse the impact of the POE-E orbit for climate applications
Jason-1 orbit comparison : POE-E versus POE-D
Outline
Content of POE-E and POE-D standard
Availability of POE-E standard (compared to orbit available in GDR-C products (POE-C/D))
Mono-mission comparison between POE-E and POE-D
Multi-mission comparison
Comparison to tide gauges
Comparison to T/S profiles

## Slide 3
New orbit data availability: comparison between POE-D| POE-E
 | POE-D (Reference ) | POE-E
Gravity model | EIGEN+GRGS.RL02bis_MEAN-FIELD | EIGEN+GRGS.RL03-v2.MEAN-FIELD
Non tidal TVG | one annual, one semi- annual, one drift terms for each year up to deg/ord 50 | one annual, one semi- annual, one bias and one drift terms for each year up to deg/ord 80
Surface forces | Radiation pressure model: thermo-optical coefficient from pre-launch box and wing model, with smoothed Earth shadow model | Radiation pressure model: calibrated semi-empirical solar radiation pressure model
DORIS | DORIS weight is reduced by a factor 10 before DORIS instrument change | SAA DORIS beacons weight is divided by 10 before DORIS instrument change
Orbit solution | Doris/Laser/GPS till cycle 169 Doris/Laser after cycle 169 | Doris/GPS till cycle 169 Doris after cycle 169
Summary of main changes between POE-E and POE-D

## Slide 4
Mono-mission comparisons
Note:
The quality of POE-E orbit solution is assessed by comparing to POE-D solution
The following analysis were done on the same ensemble of data (reference (POE-D) and test (POE-E) orbits are valid)
the study was done before delivery of the missing files for cycle 68 and 537
Sea Level Anomaly = orbit (POE-D or POE-E) – range – solid earth tide – pole tide – sea state bias (Tran 2012) – ocean tide (got 4.8) – dynamic atmosphere correction – dry troposphere correction – radiometer wet troposphere correction – filtered ionosphere correction – pseudo time tag bias – mean sea surface (CNES/CLS 2011 referenced to 7 years period)

## Slide 5
This table summarizes the thresholds to determine the impact of a new orbit in terms of climate applications and temporal scales :
Significant impact
Low impact
No impact detected
Mono-mission comparison
Jason-1 orbit comparison : POE-E versus POE-D
Climate Applications | Temporal Scales | Definition of the indicator value |  | 
 |  | Significant impact | Low impact | No impact detected
Global Mean Sea Level | Long-term evolution (trend) | Trend >0.15 mm/yr | Trend> 0.05 mm/yr | Trend< 0.05 mm/yr
 | Inter annual signals (> 1 year) | Amplitude> 0.5 mm | Amplitude> 0.2 mm | Amplitude< 0.2 mm
 | Annual and semi-annual Signals | Amplitude> 1 mm | Amplitude> 0.2 mm | Amplitude< 0.2 mm
Regional Mean Sea Level | Long-term evolution (trend) | Trend > 0.5 mm/yr | Trend> 0.1 mm/yr | Trend< 0.1 mm/yr
 | Annual and semi-annual Signals | Amplitude> 5 mm | Amplitude> 0.5 mm | Amplitude< 0.5 mm
Mesoscale | Signals < 2 months | Crossovers Variance differences > 1 cm² | Crossovers Variance differences > 0.2 cm² | Crossovers Variance differences < 0.2 cm²
Moreover, we will try in this study to indicate for each impact detected if it’s a positive (+) or a negative (-) impact.

## Slide 6
This figure shows the temporal evolution of SLA mean calculated globally.
Mono-mission comparison
Global mean sea level: trend

## Slide 7
Jason-1 |  | 
Climate Applications | Temporal Scales | Indicator
 |  | POE-E Versus Ref.(POE-D)
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Low impact detected on Global Mean Sea Level trend
0.07 mm/yr difference on the Global MSL
Impact of the orbit solutions on global MSL (with GOT4V8 tide correction) trends |  | 
Altimetry missions | POE-D | POE-E
Jason-1 | 2.91 mm/yr | 2.84 mm/yr
Mono-mission comparison
Global mean sea level: trend

## Slide 8
Low impact detected on Global Mean Sea Level trend
POE-D orbit is more homogeneous concerning MSL evolution between even and odd passes
Even passes show difference between POE-D and POE-E
MSL trend differences between Odd and Even pass for the two orbit solutions |  | 
Altimetry missions | POE-D | POE-E
Jason-1 | -0.03 mm/yr | 0.24 mm/yr
Mono-mission comparison
Global mean sea level: trend

## Slide 9
Jason-1 |  | 
Climate Applications | Temporal Scales | Indicator
 |  | POE-E Versus Ref.(POE-D)
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Low impact detected on Inter annual Signals
With GPS
GPS no longer used in POE
Geodetic phase
Mono-mission comparison
Global mean sea level: inter-annual signals
Some long-term evolution visible
0.4 mm
- 0.4 mm

## Slide 10
Jason-1 |  | 
Climate Applications | Temporal Scales | Indicator
 |  | POE-E Versus Ref.(POE-D)
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
No impact detected on Annual and Semi-annual Signals
Mono-mission comparison
Global mean sea level: annual and semi-annual signals

## Slide 11
Significant impact detected on Mean Sea Level geographic trends
Jason-1 |  | 
Climate Applications | Temporal Scales | Indicator
 |  | POE-E Versus Ref.(POE-D)
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
East-West differences between ± 1 mm/yr
Mono-mission comparison
Regional mean sea level: trend
east
west

## Slide 12
Area MSL trend differences between East [-40,130] and West [130,-40] areas for the two orbit solutions |  |  | 
Altimetry missions | POE-D | POE-E | D
Jason-1 | D= 1.38 mm/yr | D= 2.29 mm/yr | -0.91
Mono-mission comparison
Regional mean sea level: trend
Significant impact detected on long-term trends (separating east and west hemisphere)

## Slide 13
Map of Mean of Sea Surface Height at crossovers with POE-D orbit
AND
Map of Mean of Sea Surface Height at crossovers with POE-E orbit
Geographical correlated structures seem to be slightly increased with POE-E
Mono-mission comparison
Meso-scale

## Slide 14
Map of Mean of Sea Surface Height at crossovers with POE-D orbit
AND
Map of Mean of Sea Surface Height at crossovers with POE-E orbit
Geographical correlated structures seem to be slightly increased with POE-E
Mono-mission comparison
Meso-scale
POE-D
POE-E

## Slide 15
Map of Variance differences of Sea Surface Height at crossovers between POE_E orbit and Ref. : POE-D (ALL PERIOD)
Monitoring of Variance differences of Sea Surface Height at crossovers between POE_E orbit and Ref. : POE-D(TEMPORAL EVOLUTION)
Mono-mission comparison
Meso-scale
POE-E has no impact concerning short temporal scale (signals < 2 months): locally there can be variance reduction as well as variance increase

## Slide 16
Jason-1 |  | 
Climate Applications | Temporal Scales | Indicator
 |  | POE-E Versus Ref.(POE-D)
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
POE-E: No impact detected on a short temporal scale (signals < 2 months):
Locally there is variance reduction (improvement) in North Atlantic, Tasman Sea and south-west from Chile. There is small variance increase (degradation) in Indian Ocean, North-west Pacific and tropical regions.
Preliminary POE-E orbit showed a low improvement on short temporal scale (compared to POE-D)
Mono-mission comparison
Meso-scale

## Slide 17
Conclusions:
POE-E orbit is close of POE-D orbit in terms of quality.
Concerning the MSL evolution:
Low impact for the global MSL (reduction of 0.07 mm/yr), but differences between odd and even passes trend evolutions are slightly increased with POE-E
Strong impact for the regional MSL trends (+/- 1 mm/yr)
East/West gradient on geographical trends (Atlantic+Indian vs Pacific) is highlighted.
There is no clear impact on mesoscale performance at crossover points.
Jason-1 |  | 
Climate Applications | Temporal Scales | Indicator
 |  | POE-E Versus Ref.(POE-D)
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | +
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Mono-mission comparison
Conclusions